## Slide 1
DoS Attacks in Available MQTT Implementations
Investigating the Impact on Brokers and Devices, and supported Anti-DoS Protections
The 5th International Workshop on Security and Forensics of IoT - IoT-SECFOR 2021

## Slide 2: Who are we FBK Center for Cybersecurity & CNR-IEIIT
page
1/16
Umberto Morelli
Technologist @S&T FBK, Trento, Italy
Silvio Ranise Director of the Center for Cybersecurity @ FBK
&
Professor @ University of Trento
Trento, Italy
Ivan Vaccari
PhD and Research fellow @IEIIT CNR, Genova, Italy
Enrico Cambiaso
Technologist @IEIIT CNR, Genova, Italy
DoS Attacks in Available MQTT Implementations
Investigating the Impact on Brokers and Devices, and supported Anti-DoS Protections

## Slide 3: The IoT domain Security gaps and privacy issues
page
2/16
DoS Attacks in Available MQTT Implementations
Investigating the Impact on Brokers and Devices, and supported Anti-DoS Protections
Difficult or missing security features (by-design and by-default)
Incorrect adoption of
IoT protocols and developers warnings
Resource-constrained devices and security features in available IoT libraries
Low cost, time-to-market and usability preferred over adequate security

## Slide 4: The IoT domain Security gaps and privacy issues
page
2/16
DoS Attacks in Available MQTT Implementations
Investigating the Impact on Brokers and Devices, and supported Anti-DoS Protections
Difficult or missing security features (by-design and by-default)
Incorrect adoption of
IoT protocols and developers warnings
Resource-constrained devices and security features in available IoT libraries
If attackers cannot exploit those gaps to exfiltrate data, they can/will damage the service via DoS attacks
Low cost, time-to-market and usability preferred over adequate security

## Slide 5: Our approach to mitigate DoS attacks
Foster appropriate security measures via automated DoS evaluation and actionable fixes
page
3/16
DoS Attacks in Available MQTT Implementations
Investigating the Impact on Brokers and Devices, and supported Anti-DoS Protections
Investigate DoS in MQTT protocol specifications
Identify server/client-oriented DoS attacks
Test the attacks in widely-available implementations

## Slide 6: MQTT A brief introduction
page
4/16
DoS Attacks in Available MQTT Implementations
Investigating the Impact on Brokers and Devices, and supported Anti-DoS Protections
A publish-subscribe messaging protocol designed for constrained devices communicating with low bandwidth (small overhead) over unreliable networks (e.g., high latency).
TCP-based but suitable for M2M (machine to machine) telemetry
Released royalty-free in 2010, standardized by OASIS in 2014 (v3.1.1) and 2019 (v.5.0)

## Slide 7: MQTT A brief introduction
page
4/16
DoS Attacks in Available MQTT Implementations
Investigating the Impact on Brokers and Devices, and supported Anti-DoS Protections
A publish-subscribe messaging protocol designed for constrained devices communicating with low bandwidth (small overhead) over unreliable networks (e.g., high latency).
TCP-based but suitable for M2M (machine to machine) telemetry
Released royalty-free in 2010, standardized by OASIS in 2014 (v3.1.1) and 2019 (v.5.0)
Publisher (publishes on Topic1 with QoS 1)
Subscriber 1 (subscribed on Topic1 - QoS 2)
Subscriber 2
(subscribed on Topic1 - QoS 2)
Subscriber 3 (subscribed on Topic2 - QoS 2)
Broker (handle the Topic1 message queue)

## Slide 8: MQTT A brief introduction
page
4/16
DoS Attacks in Available MQTT Implementations
Investigating the Impact on Brokers and Devices, and supported Anti-DoS Protections
A publish-subscribe messaging protocol designed for constrained devices communicating with low bandwidth (small overhead) over unreliable networks (e.g., high latency).
TCP-based but suitable for M2M (machine to machine) telemetry
Released royalty-free in 2010, standardized by OASIS in 2014 (v3.1.1) and 2019 (v.5.0)
Publisher (publishes on Topic1 with QoS 1)
Subscriber 1 (subscribed on Topic1 - QoS 2)
Subscriber 2
(subscribed on Topic1 - QoS 2)
Subscriber 3 (subscribed on Topic2 - QoS 2)
Broker (handle the Topic1 message queue)
Quality of Service & persistent session
[0,1,2]

## Slide 9: MQTT The OASIS 3.1.1 and 5.0 specifications
page
5/16
DoS Attacks in Available MQTT Implementations
Investigating the Impact on Brokers and Devices, and supported Anti-DoS Protections
Summary of the OASIS recommendations
Entrust protocol developers the choice and responsibility for the specific network, privacy, authentication and authorisation technologies (especially in hostile environments).
Abnormal behaviour to investigate
Repeated connection or authentication attempts;
Abnormal termination of connections;
Topic scanning (e.g., subscribing to many topics);
Sending messages on topics with no subscribers;
Clients that connect but do not send data.
IoT Attack surface
Device or network compromise
  Attacks to data at rest or in-transit
Unhandled protocol behaviours
Denial of Service (DoS) attacks.

## Slide 10: MQTT The OASIS 3.1.1 and 5.0 specifications
page
5/16
DoS Attacks in Available MQTT Implementations
Investigating the Impact on Brokers and Devices, and supported Anti-DoS Protections
Summary of the OASIS recommendations
Entrust protocol developers the choice and responsibility for the specific network, privacy, authentication and authorisation technologies (especially in hostile environments).
Abnormal behaviour to investigate
Repeated connection or authentication attempts;
Abnormal termination of connections;
Topic scanning (e.g., subscribing to many topics);
Sending messages on topics with no subscribers;
Clients that connect but do not send data.
IoT Attack surface
Device or network compromise
  Attacks to data at rest or in-transit
Unhandled protocol behaviours
Denial of Service (DoS) attacks.
⚠
No mention to misusing message queues to perform DoS attacks:
Saturate the broker resources
Saturate the client resources (amplification attack)

## Slide 11: MQTT Exploiting message queues in out-of-the-box brokers configurations
Attacking the broker use of CPU/Network
Detect maximum message size and number of publishers; use the broker default queue value for the publishing rate
Connect and start publishing with a specific set of clients and the defined messages size and rate
page
6/16
DoS Attacks in Available MQTT Implementations
Investigating the Impact on Brokers and Devices, and supported Anti-DoS Protections
Attacking the broker Storage
Detect maximum message size
Subscribe one (or more) client/s with QoS 1; then, force the disconnection
Flood the broker with messages of the identified size

## Slide 12: MQTT Exploiting message queues in out-of-the-box brokers configurations
page
6/16
DoS Attacks in Available MQTT Implementations
Investigating the Impact on Brokers and Devices, and supported Anti-DoS Protections
Attacking the broker Storage
Detect maximum message size
Subscribe one (or more) client/s with QoS 1; then, force the disconnection
Flood the broker with messages of the identified size
-> Verify the usage of RAM and crashes
-> Verify local folders size
Attacking the broker use of CPU/Network
Detect maximum message size and number of publishers; use the broker default queue value for the publishing rate
Connect and start publishing with a specific set of clients and the defined messages size and rate

## Slide 13: MQTT Exploiting message queues in out-of-the-box brokers configurations
page
6/16
DoS Attacks in Available MQTT Implementations
Investigating the Impact on Brokers and Devices, and supported Anti-DoS Protections
Attacking the broker Storage
Detect maximum message size
Subscribe one (or more) client/s with QoS 1; then, force the disconnection
Flood the broker with messages of the identified size
-> Verify the usage of RAM and crashes
-> Verify local folders size
-> Verify the CPU usage and network throttling
-> Repeat the test with one subscriber per publisher and verify the impact on CPU/Network
Attacking the broker use of CPU/Network
Detect maximum message size and number of publishers; use the broker default queue value for the publishing rate
Connect and start publishing with a specific set of clients and the defined messages size and rate

## Slide 14: MQTT Exploiting message queues in out-of-the-box brokers configurations
page
7/16
DoS Attacks in Available MQTT Implementations
Investigating the Impact on Brokers and Devices, and supported Anti-DoS Protections
Attacking the clients (amplification attack)
Identify the maximum message size supported by the client/s
Subscribe one (or more) clients with QoS 1; then, force the disconnection.
Send a set of messages up to the broker message queue value
Re-connect the subscribers and wait to receive all messages

## Slide 15: MQTT Exploiting message queues in out-of-the-box brokers configurations
page
7/16
DoS Attacks in Available MQTT Implementations
Investigating the Impact on Brokers and Devices, and supported Anti-DoS Protections
Attacking the clients (amplification attack)
Identify the maximum message size supported by the client/s
Subscribe one (or more) clients with QoS 1; then, force the disconnection.
Send a set of messages up to the broker message queue value
Re-connect the subscribers and wait to receive all messages
-> Verify if exceeding the supported message size results in a DoS attack to the client/s
-> Verify the impact of TLS (1.2 and 1.3 when available), ACLs and MQTT v5.0.
-> Verify the reception of all messages

## Slide 16: MQTT Exploiting message queues in out-of-the-box brokers configurations
page
7/16
DoS Attacks in Available MQTT Implementations
Investigating the Impact on Brokers and Devices, and supported Anti-DoS Protections
Attacking the clients (amplification attack)
Identify the maximum message size supported by the client/s
Subscribe one (or more) clients with QoS 1; then, force the disconnection.
Send a set of messages up to the broker message queue value
Re-connect the subscribers and wait to receive all messages
-> Verify if exceeding the supported message size results in a DoS attack to the client/s
-> Verify the impact of TLS (1.2 and 1.3 when available), ACLs and MQTT v5.0.
-> Verify the reception of all messages
2 Testbeds

## Slide 17: MQTT Why assessing the out-of-the-box brokers configurations
page
8/16
DoS Attacks in Available MQTT Implementations
Investigating the Impact on Brokers and Devices, and supported Anti-DoS Protections
Country | Brokers
Korea | 54’040
China | 15’627
United States | 5’388
Austria | 3’525
Germany | 2’276
France | 1’416
Lookup of open MQTT brokers with Shodan (~80% - 99’498 MQTT brokers report Connection Code: 0)

## Slide 18: MQTT Investigating widely-adopted brokers
page
9/16
DoS Attacks in Available MQTT Implementations
Investigating the Impact on Brokers and Devices, and supported Anti-DoS Protections
 | Mosquitto | VerneMQ | EMQ X
Protocol versions | 3.1, 3.1.1 and 5 |  | 
Execution | Single-threaded | Multi-threaded | 
Secure-by-design | Block external anonymous clients since v. 2.0 (03/12/2020) | Block anonymous clients (but enforce permissive ACLs) | /
Settings that can be limited and are associated with DoS attacks | Message size and rate Size of message queues Active connections Memory usage Retained messages Keepalive (slow-DoS attack) | Message size and rate Size of message queues Active connections Memory usage (e.g., acceptors) | Message size and rate Size of message queues Active connections Memory usage (e.g., acceptors) Retained messages Keepalive (slow-DoS attack) Subscriptions

## Slide 19: MQTT Attacking the broker
chars
64
page
10/16
DoS Attacks in Available MQTT Implementations
Investigating the Impact on Brokers and Devices, and supported Anti-DoS Protections
255
MB
Attacking the RAM/Storage
255
MB
Mosquitto
v. 1.6.9
VerneMQ
v. 1.11
EMQ X
v. 4.1.5
Out-of-the-box
configuration
1MB
Attacking the CPU with two attacker setups
400
Clients
chars
64
300
Clients
59%
+ 3%
71%
+ 8%
65%
70%
+ 16%
69%
80%
1’000
1’000 / 10’000
100

## Slide 20: MQTT Attacking the broker
chars
64
page
10/16
DoS Attacks in Available MQTT Implementations
Investigating the Impact on Brokers and Devices, and supported Anti-DoS Protections
255
MB
Attacking the RAM/Storage
255
MB
Mosquitto
v. 1.6.9
VerneMQ
v. 1.11
EMQ X
v. 4.1.5
Out-of-the-box
configuration
1MB
Attacking the CPU with two attacker setups
400
Clients
chars
64
300
Clients
59%
+ 3%
71%
+ 8%
65%
70%
+ 16%
69%
80%
1’000
1’000 / 10’000
100
⚠
~ 93%
worst
case
⚠
+ 36%
worst
case

## Slide 21: MQTT Attacking the broker
chars
64
page
10/16
DoS Attacks in Available MQTT Implementations
Investigating the Impact on Brokers and Devices, and supported Anti-DoS Protections
255
MB
Attacking the RAM/Storage
255
MB
Mosquitto
v. 1.6.9
VerneMQ
v. 1.11
EMQ X
v. 4.1.5
Out-of-the-box
configuration
1MB
Attacking the CPU with two attacker setups
400
Clients
chars
64
300
Clients
59%
+ 3%
71%
+ 8%
65%
70%
+ 16%
69%
80%
1’000
1’000 / 10’000
100
⚠
~ 93%
worst
case
⚠
+ 36%
worst
case

## Slide 22: MQTT The amplification attack on clients (using Paho)
page
11/16
DoS Attacks in Available MQTT Implementations
Investigating the Impact on Brokers and Devices, and supported Anti-DoS Protections
Results with the Raspberry PIs
The use of TLS strongly affects the maximum payload size and the processing time
  Mosquitto allows sending up to 80MB payloads; VerneMQ 70MB and EMQ X* 25MB.
  A 255MB message was only received when using Mosquitto or VerneMQ without TLS.
  The processing time when using TLS is about ten times longer.
During the test, a connected client is unable to concurrently receive other messages, and it uses one of the CPU core for longer periods of times.
There is no difference in terms of performance between TLS versions (in the case of Mosquitto), MQTT v.3.1.1 and v.5.0, or if using the ACLs as authorization mechanism.

## Slide 23: MQTT The amplification attack on clients (using Paho and Mosquitto)
page
12/16
DoS Attacks in Available MQTT Implementations
Investigating the Impact on Brokers and Devices, and supported Anti-DoS Protections
chars
64
1 MB
Up to 200 Paho subscribers
Testbed
Mosquitto 1.6.9
Results
Linear increase message reception times
Messages loss with 1MB
Marginal impact of TLS
No impact of ACLs

## Slide 24: MQTT Improve the security awareness via MQTTSA
page
13/16
DoS Attacks in Available MQTT Implementations
Investigating the Impact on Brokers and Devices, and supported Anti-DoS Protections
A command-line tool that automatically detects misconfigurations in MQTT brokers and provides a report of the potential vulnerabilities and actionable mitigation strategies: recommendations and code snippets.
Open-source (available at https://github.com/stfbk/mqttsa)
Supports MQTT v.3.1.1 and 5
Allows for a comprehensive assessment
  Authentication Brute-forcing
  Credential Sniffing
  Information Disclosure
  Data Tampering
  DoS

## Slide 25: MQTT Improve the security awareness via MQTTSA
A command-line tool that automatically detects misconfigurations in MQTT brokers and provides a report of the potential vulnerabilities and actionable mitigation strategies: recommendations and code snippets.
Open-source (available at https://github.com/stfbk/mqttsa)
Supports MQTT v.3.1.1 and 5
Allows for a comprehensive assessment
  Authentication Brute-forcing
  Credential Sniffing
  Information Disclosure
  Data Tampering
  DoS
DoS
page
13/16
DoS Attacks in Available MQTT Implementations
Investigating the Impact on Brokers and Devices, and supported Anti-DoS Protections
?
Slow DoS
Flood DoS
?
Report

## Slide 26: Contributions
page
15/16
DoS Attacks in Available MQTT Implementations
Investigating the Impact on Brokers and Devices, and supported Anti-DoS Protections
Identified two simple-but-effective DoS attacks
  Target the resources of the broker.
  -> use of RAM: effective against every broker under test, in particular Mosquitto.
  -> use of Disk: effective against VerneMQ.
  -> use of CPU/Network: effective against all brokers, in particular EMQ X.
  Target the resources of possibly resource-constrained clients.
  -> Force the use of a CPU core at 100% for extended periods.
  -> Prevent the receival of additional messages.

## Slide 27: Contributions
page
15/16
DoS Attacks in Available MQTT Implementations
Investigating the Impact on Brokers and Devices, and supported Anti-DoS Protections
Identified two simple-but-effective DoS attacks
  Target the resources of the broker.
  -> use of RAM: effective against every broker under test, in particular Mosquitto.
  -> use of Disk: effective against VerneMQ.
  -> use of CPU/Network: effective against all brokers, in particular EMQ X.
  Target the resources of possibly resource-constrained clients.
  -> Force the use of a CPU core at 100% for extended periods.
  -> Prevent the receival of additional messages.
Identified 2 bugs: handling of LWT in Mosquitto, processing of heavy messages with TLS in Paho.

## Slide 28: Contributions
page
15/16
DoS Attacks in Available MQTT Implementations
Investigating the Impact on Brokers and Devices, and supported Anti-DoS Protections
Identified two simple-but-effective DoS attacks
  Target the resources of the broker.
  -> use of RAM: effective against every broker under test, in particular Mosquitto.
  -> use of Disk: effective against VerneMQ.
  -> use of CPU/Network: effective against all brokers, in particular EMQ X.
  Target the resources of possibly resource-constrained clients.
  -> Force the use of a CPU core at 100% for extended periods.
  -> Prevent the receival of additional messages.
Identified 2 bugs: handling of LWT in Mosquitto, processing of heavy messages with TLS in Paho.
Identified the security parameters associated with DoS in three widely used and reviewed open-source MQTT brokers: Mosquitto, VerneMQ and EMQ x.

## Slide 29: Contributions
page
15/16
DoS Attacks in Available MQTT Implementations
Investigating the Impact on Brokers and Devices, and supported Anti-DoS Protections
Identified two simple-but-effective DoS attacks
  Target the resources of the broker.
  -> use of RAM: effective against every broker under test, in particular Mosquitto.
  -> use of Disk: effective against VerneMQ.
  -> use of CPU/Network: effective against all brokers, in particular EMQ X.
  Target the resources of possibly resource-constrained clients.
  -> Force the use of a CPU core at 100% for extended periods.
  -> Prevent the receival of additional messages.
Identified 2 bugs: handling of LWT in Mosquitto, processing of heavy messages with TLS in Paho.
Identified the security parameters associated with DoS in three widely used and reviewed open-source MQTT brokers: Mosquitto, VerneMQ and EMQ x.
Integrate the attacks and security parameters in MQTTSA to increase the security awareness in MQTT-based deployments.

## Slide 30: Future work
page
16/16
DoS Attacks in Available MQTT Implementations
Investigating the Impact on Brokers and Devices, and supported Anti-DoS Protections
Identify DoS attacks in MQTT 5
Test additional MQTT brokers
and clients
Automatically tailor tests according to hardware capabilities

## Slide 31: Future work
page
16/16
DoS Attacks in Available MQTT Implementations
Investigating the Impact on Brokers and Devices, and supported Anti-DoS Protections
Identify DoS attacks in MQTT 5
Test additional MQTT brokers
and clients
Automatically tailor tests according to hardware capabilities
For further information and support on MQTTSA,
I’m always available at umorelli@fbk.eu :)